## Slide 1: Test proposals for CAT Surveillance panel with PC9 &10 fuels from an alternate supplier

## Slide 2: Haltermann Solutions Diesel fuels ( PC-9 and 10) and Combustion Behavior
We will provide Chemical analysis of our fuels to show that our fuels not only meet the specifications but are chemically identical in terms of speciated components that affect major test variables.
Diesel fuel combustion is characterized by diffusion flames in an oxygen rich environment where chemical kinetics play a significantly lesser role. Most diesel engine lube tests worldwide do not consider fuel to be a major factor as long as fuel meets the specs. We do not think CAT panel tests are any different.
Since the industry has developed a large database over the years with only one fuel source, we are willing to verify the data with limited testing that shows the data we develop is within the range of the existing dataset.

## Slide 3: CAT panel -1N &1P Single cylinder engine tests
Piston and ring grove deposits and oil consumption measurements using reference oil and the candidate fuel
Test Proposal
Conduct two tests with reference oil and Candidate fuel and verify whether the test data falls within the current range of the current test database.
Submit the data to the panel for approval of the candidate fuel.
Test duration: 1N: 200 hours, 1P: 360 hours
Oil qty: 10 gallons/test
Fuel qty: 1000 gallons of PC-9 per test
Measurements: Oil consumption and deposit rating

## Slide 4: CAT panel – C13 tests
Piston and ring grove deposits, ring sticking and oil consumption measurements using reference oil and the candidate fuel
Test Proposal
Conduct two tests with reference oil and Candidate fuel and verify whether the test data falls within the current range of the current test database.
Submit the data to the panel for approval of the candidate fuel.
Test duration: 500 hours
Oil qty: 25 gallons/test
Fuel qty: 13000 gallons of PC-10 per test
Measurements: Oil consumption and deposit rating

## Slide 5: CAT panel – COAT tests
Percentage Aeration measurements using reference oil and the candidate fuel
Test Proposal
Conduct two tests with reference oil and Candidate fuel and verify whether the test data falls within the current range of the current test database.
Submit the data to the panel for approval of the candidate fuel.
Test duration: 50 hours
Oil qty: 30 gallons/test
Fuel qty: 500 gallons of PC-10 per test ~*Estimate
Measurements: Oil Aeration