## Slide 1: Build Workshop Day #1 Meeting Notes Greg/Suzanne/Patrick/Sean/Jacob/Daniel/ Chris/ Jose/ Pete/Jim G.

## Slide 2: 1. Fuel Cooler/Air Compressor Lines
Fuel Cooler is currently being used. It will no longer be used in the future. All of the new service kits will come with the fuel block off plate.
  Then we will need to provide a connection between the air compressor ports. (add pictures later)
  ACTION ITEM – Patrick/Sean will summarize edits for the procedure to outline the new build procedure related to these parts (and the new connection line)
  (Fuel filter comes in the TEI kit, we might need 2 TEI kit numbers, one for the old kit module and one for the new kit module.

## Slide 3: 2. Coolant Filter
  Detroit currently does not use a coolant filter in their current production engines. (Detroit also advises customers to remove the coolant filter from their older model year engines – no block off plate, just to remove the filter) @Suzanne to add TS-Letter #/Link
  Need to discuss if we should keep or remove the coolant filter for the future of the DD13 Scuffing Test. [Not urgent just optional and open for discussion.]
  Note: the old oil module and coolant filters will always be available in service.
  Currently DD13 Scuffing Test has the coolant filter replaced at the beginning of each test.

## Slide 4: 3. Rebuilding the Head – Not standardized between labs
LZ/SWRI/IAR do not replace the valves or seats because DDC does not have service kits/parts available for that.
LZ does replace keepers, springs, seals, but SWRI/IAR do not. LZ started doing this ~ 2 years ago. This might not be needed.
IAR/SWR) they replace the head if there is a leaking valve seal or valve guide then they will replace the head.
Team decided to leave it at lab discretion.

## Slide 5: 4. Mark the front of the Liner during build
Currently the procedure does not have a way outlined to mark the front of the liner during the liner installation.
The front of the liner needs to be identified during installation.
ACTION ITEM – Add section to 8.5 Assembly Instructions, 8.5.8 Liners…etc.
The front of the liner is marked for the rating process.

## Slide 6: 5. Fix instructions in 8.1.10 Cylinder Liners
Under 8.1.10 Cylinder Liners, remove point (6).
  “(6) after installation wipe clean with heptane”
Need to add a timeline for the cleaning process for the liners (Oil immediately after cleaning and install the liners. If the oiled liners have been sitting for more than 24 hours, then repeat the cleaning with heptane (step 4)/oil process (step 5)).
  ACTION ITEM – Update Cleaning Liners section.
  *Note: we might want to consider adding something to the procedure to make sure that the coolant side of the liner is not oiled during the installation process. Review DDCSN.com process to see if it is documented, if not, we can add it to the procedure.

## Slide 7: 6. Piston Cleaning Process
IAR – Solvent bath, then use heptane, then air gun for 8-10 minutes each. (no wiping)
SWRI – Solvent cleaner (not sure if bath or spray), then blow dry with compressed air until dry.
LZ – Use an air gun to remove any packaging or debris, and then wipe with heptane and air dry.
We have discussed solvent baths and how the solvent is difficult to get out of all of the ports. Double check with Michael Thiel to see if the coating can be removed by specific chemicals.
ACTION ITEM - Need to align on a common cleaning procedure.

## Slide 8: 7. Cleaning the “Oil Holes” on the Connecting Rods
Differences in how the oil holes are cleaned on the connecting rods.
LZ – Stiff Nylon Bristle brush
IAR – Q-Tip
SWRI – Nothing after part comes out of the part washer.
ACTION ITEM – Need to align on a cleaning process.

## Slide 9: 8. Cylinder Heads
All heads are the new scalloped head.
The part was released as a new part number and that it was backwards compatible.
However, the labs explained that they sometimes receive re-man older heads when they try to order the new heads.
Only use new scalloped heads moving forward and try to avoid using re-man heads.

## Slide 10: 9. Cylinder Head – Installation
LZ – using a 3 step torque process and lubricating the bolts before hand.
  75, 125, 147 then 90, 90
IAR
  147, then 147, then 90, 90
SWRI
  147, then 147, then 90, 90
Team decided that this is not critical as long as the end torque is reached.

## Slide 11: 10. Oil Pump Change Interval
Procedure – replace the oil pump after a maximum of 400 running hours (8.2.2)
LZ – 2 tests maximum
IAR – Every test
SWRI – Every test
Comments:
  Difficult to track.
  If the test scuffed, the pump is sometimes damaged.
  Labs commented that the oil pump is not that expensive.
  Part number of oil pump has changed many times, need to find out which one is most recent.
Need to decide if we are going to change to every test or stay the way we are.

## Slide 12: 11. Updates for TEI kits
Add - Fly wheel bolts
Add - Oil Pump??
Remove – Coolant Filter??

## Slide 13: 12. Camshaft/Camframe
@Suzanne to check for a TS letter or service letter for looking at camshaft/camframe wear and deciding what is acceptable or not.
@Suzanne to add pictures.

## Slide 14: 13. Washing/Oiling Rockershafts Before Assembly
LZ – use air to remove any packaging, no washing, then oil the bushing only.
IAR – washes and oils the rocker shaft.
SWRI – just oil (no washing)
Need to discuss adding a cleaning process to the procedure.
Review parts on day #2

## Slide 15: 14. Fuel Rail Pressure Sensor
Do not put the fuel rail pressure sensor in the sonicator with solvent.
Consider adding this to the procedure to help future labs.

## Slide 16: 15. Camshaft Phaser Wheel
Ask supplier if this part is available separate from the camshaft.
Ask about internal specification for run out of the camshaft phaser. (Ask Adam Miller)

## Slide 17: 16. Power Service Literature
Ask Greg if we can get power service literature for Intertek. (SWRI and LZ already have it).

## Slide 18: 17. Driveline
LZ – use double U joint drive shafts
IAR – use double U joint drive shafts and centamax coupling system
SWRI - centamax coupling system
Need to discuss.