## Slide 1: Mack T12 LTMS20160222 New Parts and ICF Review
Jim Rutherford
03/02/2016

## Slide 2: Contents
Just a few additional items based on many conversations
  OC corrected Pb and Pb2 using lower slope below 65
  Various traditional ICFs

## Slide 5
OC, Liner Wear, and TRWL ICFs

## Slide 6
Pb and Pb2 Oil Consumption Correction
Correction Factor for ΔLead at EOT—For all tests after April 5, 2011, determine the final ΔLead at EOT result by applying the correction:
    if OC100–300 >65.0, then ΔLeadFinal = e ln(Δlead)+(65-OC100–300) X 0.03088,
    if OC100–300 ≤65.0, then ΔLeadFinal =ΔLead,
  where
    ΔLeadFinal = final ΔLead at EOT,
    ΔLead = value calculated per Eq 2, and
    OC100–300 = average oil consumption from 11.6.6.
Correction Factor for ΔLead(250-300) h—For all tests after April 5, 2011, determine the final ΔLead(250-300)h result by applying the correction:
    if OC100–300 >65.0, then ΔLead(250-300)Final = e ln(ΔLead(250-300))+(65-OC100–300) X 0.04021,
    if OC100–300 ≤65.0, then ΔLead(250-300)Final =ΔLead(250-300),
  where
    ΔLead(250-300)Final = final ΔLead(250-300) h,
    ΔLead(250-300) = value calculated per 11.6.5, and
    OC100–300 = average oil consumption from 11.6.6.