## Slide 1: Sequence X Severity Task Force
Meeting Minutes
April 13, 2021
April 20, 2021
Alfonso Lopez

## Slide 2: Attendance
Michael Deegan
Rich Grundza
Christian Porter
Christine Eickstead
Amol Savant
Joe Gleason
George Szappanos
Jason Soto
Alfonso Lopez
Travis Kostan

## Slide 3: Minutes / Action Items/(04/13/21)
Revisited Ln log transform
  Stats group still formulating a plan to remove the effects of the drop to infinity as engineering units approach zero.
George presented three build concerns. See Slides 4-6 for concern and recommended action.

## Slide 4
Concern 1:
LZ’s NEW blocks come in at 9-13 Ra surface finish (procedure spec) using a SJ-410 profilometer.
And for us, re-honing a used block with a 320 grit hone results in 6-9 Ra. That’s quite a large range/change and precludes reusing blocks.
The options seem to be:
Maintain the original 9-13 range, add detail about profilometer
  Both 240 and 320 grit hones are found to be acceptable…
  New blocks also prepped with a fresh hone
  Revise max number of hone ?
Widen the range to accept smoother re-honed/used blocks
  Jason had suggested 7-11 Ra
  but to accommodate rougher new blocks this should be 7-13 Ra
  potentially adds variability to test
Re-hone NEW blocks and revise spec to 7-11 Ra
  might shift severity
  adds some complexity

## Slide 5
Concern 2
8.19.3.3 Install the pistons and connecting rods with the notches facing the rear.
When new engines are disassembled the notch does face to the front of the engine.
LZ Recommends rewording: Install the pistons with arrows facing forward and connecting rods with the notches facing the front.

## Slide 6
Concern 3
6.2.2.1 Crankshaft and bearings, connecting rods and bearings, pistons, camshafts, timing-chain covers, cylinder blocks, cylinder-head assemblies, turbocharger, and fuel injectors can also be used for a maximum of six tests provided they remain serviceable. However, keep these parts together as a set for all six tests.
This implies that if a turbocharger or fuel injector needs replacement sometime during the allowable 6 runs, the test engine can no longer be used.
LZ Recommends: Clarification and Revisiting the idea of what parts can be replaced without affecting the allowable runs per engine
Suggested wording: * remove red items?

## Slide 7: Minutes / Action Items/(04/13/21)
Ball Hone Discussion
  LZ not honing new blocks, all other labs honing both new and used to reach surface finish.
  Amol pointed out that we are looking at Ra only and there may be other surface finish parameters that are being affected
  Christine recommended ball honing both new and used blocks for ensure all surface finish parameters remain the same – not just Ra.
  The procedure allows up to 24 hones from one ball hone.
  Jason to experiment with 240 grit to see if the 9-13 Ra can be met.

## Slide 8: Minutes / Action Items/(04/20/21)
Transform Discussion
  Travis and Martin gave the group an update from the stats group. There are concerns with changing the transform or adding a correction factor. The stats group will report out on different options at the next SP meeting.
Travis presented a slides on TAN, TBN and water content levels by lab and there is no distinct correlation to severity.
Amol informed the group that his experimental test with a BB stack orifice plate was on target with oil 1011. CHST = .1258
  Amol reported CC pressure in both 1st and second stage of more than one kpa.
  Jason has also seen an increase in severity using the orifice plate.
  Amol will run another test using oil 270.
  The orifice plate may be allowing more condensation and drain back into the crankcase. He reported seeing more sludge and emulsion in the engine at EOT.
  Amol to send a chemistry report on his test when he receives the data

## Slide 9: Minutes / Action Items/(04/20/21)
Torsional vibration discussion
  A review of the stand components is needed. The harmonic balancer has changes with newer engine batches. Labs to report what balancer is being used
  Clutch pack is designed to absorb torsionals. OHT will be asked is there has been a change and how the stiffness is measured in the pressure plate.
  The driveshaft has a specified stiffness. Has it changed? Group to investigate and consult vendor.
Fuel batch discussion
  Christine to ask her fuel group if there are other properties we can look at that are not on the CoA.