## Slide 1: Sequence VIII LTMS Version 2 review
LTMS TF SS
May 11, 2010

## Slide 2: Reference oil data summary
Includes 205 chartable data
Four (4) test laboratories (A, B, C and D)
  A – 102 chartable
  B – 86 chartable
  C – 4 chartable
  D – 13 chartable
Latest reference oil result is March 1, 2010
Focus

## Slide 3: LTMS VERSIOn 2
Primary Parameter: Total Bearing Weight Loss
Secondary Parameter: 10-hour Stripped Viscosity
Shewhart Chart of Prediction Error ei = Yi - Zi-1 |  | 
Limit Type | Limit | 
Level 3 | 2.066 | 
Level 2 | 1.734 | 
Level 1 | 1.351 | 
Undue Influence | 2.066 | 
EWMA of Standardized Test Result: Zi |  | 
Limit Type | Lambda | Limit
Level 2 Lower | 0.2 | TBD by SP
Level 2 Upper | 0.2 | TBD by SP
Level 1 | 0.2 | 0

## Slide 4: Review of alarms and actions
Chart: Fate of Sequence VIII Calibration Attempts from LTMS Dataset - Current System
| Aborted | Invalid | Failed | Success
 | 6.689 | 28.0936 | 12.0401 | 53.1773

## Slide 5: Review of alarms and actions
Chart: LTMS Alarms and Reference Period Extensions in Sequence VIII (TBWL Primary)
| B | A | A+B
Extended 20% - New | 7 | 5 | 12
Extended 40% - New | 9 | 31 | 40
Reduced Interval - New | 11 | 3 | 14
Unacceptable - New | 5 | 3 | 8
Unacceptable - Current | 16 | 1 | 17

## Slide 6: Prediction error shewhart
Chart: TBWL ei Shewhart Chart by Lab

## Slide 7: Prediction error
Chart: Candidate Oil Test Result Target Variability in Sequence VIII
| B | A | All Labs
New System | 1.2276 | 0.98087 | 1.0976
Current System | 1.3676 | 0.97585 | 1.1681

## Slide 8: Prediction error
Chart: Candidate Oil Test Result Target Variability in Sequence VIII
| B | A | All Labs
New System | 1.4739 | 1.059 | 1.2622
Current System | 1.4592 | 1.0671 | 1.2581

## Slide 9: Effective pass limit
Test Sequence
Chart: Effective Pass Limit Given Severity Adjustment in Lab A

## Slide 10: Effective pass limit
Test Sequence
Chart: Effective Pass Limit Given Severity Adjustment in Lab B