## Slide 1: Chain Wear Precision Matrix Operational Data Plots Phases 1 & 2
Kevin O’Malley
The Lubrizol Corporation
October 19, 2016

## Slide 2
Labs identified “erroneous” data after operational data review of Chain Wear Operational Data Plots to Identify Erroneous Data 9-16-16.pptx in September
Plots of Phase 1 and Phase 2 data are shown in the appendix
  Data identified as “erroneous” have been removed
  Where appropriate, additional plots are included which zoom in on operational parameters to obtain a better view of the data. These are labeled “Zoomed In” on the top of the slides
Slides 3 through 13 summarize lab differences in the level of within-test variability
Slides 14 through 23 highlight operational parameters in which the labs differ in magnitude
Analyses of ramp data are being addressed separately
Overview

## Slide 3
Variability Differences – Ramping in PH1 & PH2
Labs A & G
Cycles are overlaid
Phase 1
Labs A and G appear to be ramping at the start of each Phase 1 cycle
This may mean ramping isn’t complete when phase 1 starts
It may also mean that ramp data was included in phase 1 data by accident
The ramping is not observed in every 6th cycle at lab G (cycles 1, 7, 13, etc.)

## Slide 4
Variability Differences – Ramping in PH1 & PH2
Labs A & G
Cycles are overlaid
Phase 1
Labs A and G appear to be ramping at the start of each Phase 1 cycle
This may mean ramping isn’t complete when phase 1 starts
It may also mean that ramp data was included in phase 1 data by accident
The ramping is not observed in every 6th cycle at lab G (cycles 1, 7, 13, etc.)
Note: 1 cycle between 50C & 70C not shown

## Slide 5
Phase 1:
Lab A Stand 27 appears to be ramping at the start of each cycle. This is observed in both coolant in and out temperatures
This may mean ramping isn’t complete when phase 1 starts.
It may also mean that ramp data was included in phase 1 data by accident
Variability Differences – Ramping in PH1 & PH2
Lab A
Cycles are overlaid on one another

## Slide 6
Barometric pressure is fairly constant within each cycle.
It’s cycle-to-cycle differences that cause the overall variability to be larger
This is mainly observed in labs D and A, but does show up in a few tests at lab G
Variability Differences – Cycle to Cycle Consistency
All Labs
Cycles are overlaid on one another
Phase 1
Phase 2

## Slide 7
Within a cycle ambient temp is fairly consistent
It’s cycle-to-cycle differences that cause the overall variability to be larger
Variability Differences – Cycle to Cycle Consistency
All Labs
Cycles are overlaid on one another
Phase 1
Phase 2

## Slide 8
Within a cycle fuel temp variability is fairly consistent
It’s cycle-to-cycle differences that cause Labs A & G to have higher overall variability
Variability Differences – Cycle to Cycle Consistency
Labs A & G
Cycles are overlaid on one another
Phase 1
Phase 2

## Slide 9
Within a cycle coolant pressure variability is small
It’s cycle-to-cycle differences that cause Lab G’s overall variability to be larger than the other labs
Variability Differences – Cycle to Cycle Consistency
Lab G
Cycles are overlaid on one another
Phase 1
Phase 2

## Slide 10
Within a cycle fuel pressure variability is fairly consistent
It’s cycle-to-cycle differences that cause Lab A’s overall variability to be larger than the other labs
Variability Differences – Cycle to Cycle Consistency
Lab A
Cycles are overlaid on one another
Phase 1
Phase 2

## Slide 11
Lab D has lower oil gallery temp variability in their last 2 tests
Variability Differences
Lab D
Phase 1
Phase 2
Higher variability attributed to: 1st and 4th test in Phase 1; 1st test in Phase 2
Cycles are shown contiguously
Most variability in inlet air pressure observed in Lab D tests
Lab D consistently has most variability; A1 variability attributed to cycle-to-cycle consistency

## Slide 12
Lab A has the least PH2 exhaust back pressure variability compared to other labs
Variability Differences
Lab A
Phase 1
Phase 2
Cycles are shown contiguously
Stand 27 has higher variability
Lab A has lowest variability in actual exhaust (B) camshaft position

## Slide 13
Lab G operates at engine speed 2500 + ~10 to ~20 while the other labs operate at + ~5 to ~10
Variability Differences
Lab G
Phase 1
Phase 2
Increased variability at Lab G due to humidity excursions
Variability in Lambda is higher at Lab G
Cycles are shown contiguously
Intake air temp variability highest in stand 93

## Slide 14
Less variability in blowby outlet temp is observed in 4th test compared to first 3; accompanied by slight change in temp
At 30 cycle in Lab D’s 3rd test it appears a control change was made resulting in:
lower fuel pressure
higher boost pressure
higher boost absolute pressure
lower accelerator pedal position
Lab Differences
Lab D Control Change
Phase 1
Phase 2
Cycles are overlaid

## Slide 15
Lab D exhibits higher barometric pressure than other labs
Lab Differences
Lab D
Phase 1
Phase 2
Lab D lower oil gallery pressure;
Lab D 4th test more aligned with other labs;
Lab A stand 8 1st test lower
Lab D lower oil head pressure;
Lab D 4th test more aligned with other labs;
Lab A stand 8 1st test lower;
Lab A stand 27 4th test lower
Cycles are shown contiguously
Lab D fist 2 tests higher oil out temperature

## Slide 16
Lab D exhibits higher pre-intercooler air pressure (phase 2: only last 2 tests)
Lab Differences
Lab D
Phase 1
Phase 2
Cycles are shown contiguously
Lab D phase 2 coolant in temp slightly lower
Lab D higher boost pressure (in phase 2 it’s only the last 2 tests);
Note: A27 also higher in phase 2
Lab D operating at upper end of range observed across labs

## Slide 17
Lab D has lower MAP on some tests
Lab Differences
Lab D
Phase 1
Phase 2
Cycles are shown contiguously
Lab D higher blowby heat exchanger coolant in, on average, in PH1; lower in PH2
Lab D 1st test has lower PH2 ignition timing advance for #1 Cylinder

## Slide 18
First 2 lab D tests have lower engine coolant temp; 2nd test in A8 also lower
Lab Differences
Lab D
Phase 1
Phase 2
Cycles are shown contiguously
Lab D generally has higher fuel rail pressure

## Slide 19
First test in both stands exhibit lower fuel pressure
Lab Differences
Lab A
Phase 1
Phase 2
Cycles are shown contiguously
A8 has higher Phase 2 blowby heat exchanger coolant l/m
Tests 3 and 4 in stand 8 are slightly lower;
Note: Lab D slightly lower in phase 1

## Slide 20
G95 has slightly lower ambient temp
Lab Differences
Lab G
Phase 1
Phase 2
Cycles are shown contiguously
G95 has slightly higher PH2 turbocharger wastegate duty cycle;
Lab D’s 2nd test also higher

## Slide 21
Lab D lowest Lambda;
Stands 8 and 27 differ.;
Last 2 tests in stand 93 are lower
Lab Differences
Multiple Labs
Phase 1
Phase 2
D and G95 lowest exhaust temp
G93 has highest temp
Phase 1:
G highest temp; A27 and D lowest
Phase 2:
Cycles are shown contiguously
G95 slightly higher Crankcase kPaG
Phase 1:
G95 highest pressure; A8 lowest
Phase 2:
PH2: A27 and D have lower absolute throttle position

## Slide 22
Lab D generally lower abs load value%; Lab G generally higher in PH2
Lab Differences
Multiple Labs
Phase 1
Phase 2
Lab D slightly lower intake manifold abs pressure, especially 1st test PH2
Labs A and G differ;
Labs D & A similar after 30th cycle of 3rd test;
Labs D & G similar prior to 30th cycle 3rd test
Cycles are shown contiguously
PH1: D has highest boost abs pressure and G is slightly higher than A;
PH2: D and A27 highest, G95 and A8 slightly lower than A27

## Slide 23
Labs A and D don’t have negative actual intake (A) camshaft position data
Lab Differences
Multiple Labs
Phase 1
Phase 2
Cycles are shown contiguously
Labs G generally has higher exhaust (B) camshaft position actuator duty cycle;
Stands at lab A differ

## Slide 24
APPENDIX

## Slide 26
ZOOMED IN

## Slide 28
ZOOMED IN

## Slide 30
ZOOMED IN

## Slide 32
ZOOMED IN

## Slide 41
ZOOMED IN

## Slide 47
ZOOMED IN

## Slide 50
ZOOMED IN

## Slide 53
ZOOMED IN

## Slide 61
ZOOMED IN

## Slide 63
ZOOMED IN

## Slide 66
ZOOMED IN

## Slide 73
ZOOMED IN

## Slide 77
ZOOMED IN

## Slide 79
ZOOMED IN

## Slide 81
ZOOMED IN

## Slide 83
ZOOMED IN

## Slide 85
ZOOMED IN

## Slide 87
ZOOMED IN

## Slide 92
ZOOMED IN

## Slide 97
ZOOMED IN

## Slide 108
ZOOMED IN

## Slide 111
ZOOMED IN

## Slide 120
ZOOMED IN

## Slide 122
ZOOMED IN

## Slide 124
ZOOMED IN

## Slide 126
ZOOMED IN

## Slide 128
ZOOMED IN

## Slide 131
ZOOMED IN

## Slide 138
ZOOMED IN

## Slide 142
ZOOMED IN

## Slide 144
ZOOMED IN